# Creating a Nomogram
[Note: It is not necessary to read this document to use nomogen. It is for reference only.
Since nomogen is experimental, some of the ideas here have been tested and abandoned, some others have yet to be tested, what’s left should (hopefully) describe the internals of nomogen.]
Use well known engineering principles:
- Use tried and tested components and techniques.
  Just hook together the good work of others.
- use brute force. (given to us by Moore’s law.)
Method outline:
- Approximate each scale line with a polynomial,
- estimate the cost of each approximation. The cost is a function of the error in the scale curves and how well the curves fit into the allocated area
- use python’s SciPy numerical optimisation library to minimise this cost,
- use pynomo libraries to scale and plot the nomogram.
The nomogram is calculated to fit inside a unit square. This is achieved by one of
1. tie the ends of the outer scales to the corners of the unit square (current scheme)
2. use a cost function that rewards the nomogram as it gets larger up to the boundary of the unit square, and then penalises it if it extends outside the unit square. (possible future scheme)
The following assumes we are to generate a nomogram for the function w=w(u,v). The u, v & w scales are respectively on the left, right and middle of the nomogram.

The x and y coordinates of the value u on the u scale are given by the parametric functions xu(u) and yu(u), and so on for the other scales.
Our goal is to use numerical techniques to find polynomials that closely approximate xu(u), etc.
The nomogram is generated on a unit square, which PyNomo scales to the required size when it creates the output.

## The Polynomials
Each scale line is defined by a Chebyshev polynomial, not with a set of coefficients like u_x = sum from { { k = 0 } } to { N } { {%alpha_i} T_i(u)} , but by interpolating its values at so-called Chebyshev nodes.
A major problem with using equally spaced nodes to approximate the scale lines (or any function in general) is that the approximation can deviate wildly near the end points – see reference [6]. (This is known as Runge’s phenomenon and is intuitively plausible since there are no nodes beyond the end points to constrain the approximating function.)
Polynomials defined at the Chebyshev nodes counter this by bunching the nodes near the ends, so (very nearly) minimising the maximum error.
 If there are N+1 Chebyshev nodes for the u curve, they occur at the points
u_k = u_min + ( {u_max - u_min} )(1 - cos( {k*%pi} over N ))/2, " where k = 0,1, .. N
These nodes can be interpreted as the projection from a semi-circle onto the u axis of equally spaced angles, so node uk is the projection from an angle k%pi over N :

This scheme concentrates the nodes near the ends which keeps the approximation close to its correct value.
If we have values of the function at these points, there is a unique N-degree polynomial that fits these points.
We determine the coordinates of the u, v & w curves at the Chebyshev nodes, and from there generate the curves of the nomogram.
Taking the u scale as an example, we need to define the function ux(u). Given xk, the x coordinate of the node uk, we can efficiently interpolate the x coordinate of any point u as follows:
(This code assumes N is odd)
    if u is one of uk then
        use xk & yk, the known values for node k
    else
        sumA = (x0/(u-u0) + xN/(u-uN))/2
        sumB = (1/(u-u0) + 1/(u-uN))/2
        for k in 0 .. N
        t = 1/(u-uk)
        sumA = t*xk - sumA
        sumB = t - sumB
        x(u) = sumA / sumB

The y coordinate, yu(u) is very similar, as are the functions for the other scale lines.
See references [4] and [5], which also describe how to calculate the derivatives of the function.

## Basic Nomogram Calculations
Suppose we have 3 points, A, B & C in an x-y coordinate system:

(xB,yB)
(xA,yA)
(xC,yC)

x
y
A
B
C

The area inside the triangle ABC is
Area " = " 1 over 2 ({(x_A - x_B)} { (y_A - y_C) } " " - " " {(x_A - x_C)} { (y_A - y_B) } )
(This is the vector cross product of the 2 line segments. It is calculated like a determinant, but technically, it is not a determinant.)
Alternatively, the area can be given by
Area " = " 1 over 2 ~ lline AB rline ~ lline AC rline ~ sin(%theta) ,
where |AB| and |AC| are the lengths of the line segments AB & AC, and θ is the angle between the two line segments.
The points A,B,C lie on a straight line if the Area = 0, or
{(x_A - x_B)} { (y_A - y_C) } " " = " " {(x_A - x_C)} { (y_A - y_B) }
x_A y_B + x_B y_C + x_C y_A - x_A y_C - x_B y_A - x_C y_B " " = " " 0	(1)

The distance of the point C from the line AB is
d " = " 2*{Area(ABC)} over {base line AB}
d " = " { {(x_A - x_B)} * { (y_A - y_C) } " " - " " {(x_A - x_C)} * { (y_A - y_B) } } over sqrt{ {(x_A - x_B)} ^{2} + { (y_A - y_B) } ^ 2}	(2)

We wish to generate a nomogram for the formula
w = w(u,v), " where " u_min "<= " u " <= " u_max ", " v_min "<= " v " <= " v_max
The scale lines are approximated by parametric curves with coordinates given by polynomial functions of u, v and w:
 u = (xu, yu), where xu = xu(u) and yu = yu(u)
and so on for the v & w scale lines.
This gives us functions xu(u), yu(u), etc., and since for any u & v such that w = w(u,v), the nomogram points must lie on a straight line, we can write
 (x_u-x_v) over (y_u-y_v) " = " (x_u-x_w) over (y_u-yw) or rearranging
x_u y_v - x_u y_w - x_v y_u + x_v y_w + x_w y_u - x_w y_v " = " 0
This is an alternative derivation of (1) above, and is equivalent to the determinant:
left lline matrix{u_x(u) # u_y(u) # 1 ## v_x(v) # v_y(v) # 1 ## w_x(w) # w_y(w) # 1} right rline
which can be used as input for a type 9 nomogram in pynomo (see references [1] and [2]).
Given the function w=w(u,v), and assuming we have approximate functions for the scale lines as above, we have the x & y coordinates of points u, v and w. Since these functions are only approximate, the point w on the w scale does not lie exactly on the index line connecting u & v, as shown below.
This error is shown as e in the following diagram:

u
w
v

u
v
w

e
The strategy to generate a correct nomogram is to jiggle the equations of the scale lines until e converges to zero. (The python SciPy optimisation libraries do this for us.)
## Derivatives of the scale lines
We have just seen that we want the error in the scale lines to be zero. Now we want to ensure the scale lines do not head off in a direction that makes the error larger.
Consider a small segment of the u, v & w scale lines as follows:

u
w
v

B

dw
B

A

The index line AA intersects the scale lines at (xu,yu), (xv,yv) & (xw,yw).
The index line BB is a small perturbation of AA by an amount du, keeping its intersection with the v scale line unchanged.
  We assume that index line AA has no error, and we want to find the conditions that guarantee that line BB also has no error.
The scale lines are defined by the equations xu = xu(u), etc., and the function w is defined as w = w(u,v)
 We can write the following since the intersection points on the lines are co-linear:
(x_u - x_v) ( y_w - y_v ) " = " ( x_w - x_v ) ( y_w - y_v )	(3)

(x_u + {dx_u} over {du}du - x_v) ( y_w + {dy_w} over {dw}dw - y_v ) " = " ( x_w + {dx_w} over {dw}dw - x_v ) ( y_u + {dy_u} over {du}du- y_v )	(4)

Expanding (4):

" " (x_u + {dx_u over du}du - x_v) y_w ~+~ (x_u + {dx_u over du}du - x_v) {dy_w over dw}dw ~-~ (x_u + {dx_u over du}du - x_v) y_v newline " = " ( x_w + {dx_w over dw}dw - x_v ) y_u ~+~ ( x_w + {dx_w over dw}dw - x_v ) {dy_u over du}du ~-~ ( x_w + {dx_w over dw}dw - x_v ) y_v
Dropping second order terms & substituting (3):
y_w {dx_u} over {du}du " + " (x_u - x_v) {dy_w over dw}dw " - " y_v {dx_u over du}du " = " y_u {dx_w over dw}dw " + " ( x_w - x_v ) {dy_u over du}du " - " y_v {dx_w over dw}dw
(y_w - y_v) {dx_u over du}du " + " (x_u - x_v) {dy_w over dw}dw " = " (y_u - y_v) {dx_w over dw}dw " + " ( x_w - x_v ) {dy_u over du}du
We also know
dw " = " { partial w } over {partial u} du " + " { partial w } over {partial v} dv ,
and since in this case dv = 0, we have:
dw " = " { partial w } over {partial u} du , so substitute this and rearrange:
{ partial w } over {partial u}((x_u - x_v) {dy_w over dw} " - " (y_u - y_v) {dx_w over dw}) " = " ( x_w - x_v ) {dy_u over du} " - " (y_w - y_v) {dx_u over du}	(5)

There is a similar equation for an index line perturbed along the v scale line while keeping the u value constant:

{ partial w } over {partial v}((x_u - x_v) {dy_w over dw} " - " (y_u - y_v) {dx_w over dw}) " = " ( x_u - x_w ) {dy_v over dv} " - " (y_u - y_w) {dx_v over dv}	(6)

Now move an index line by a small amount, but keep the w point unchanged:

A
A
B
B

dv
du

As before, we can write:
{ x_u - x_w } over { y_u - y_w } ~=~ { x_w - x_v } over { y_w - y_v } , and

{ x_u + dx_u over du du - x_w } over { y_u + dy_u over du du- y_w } ~=~ { x_v + dx_v over dv dv- x_w } over { y_v + dy_v over dv dv - y_w }

( x_u + dx_u over du du - x_w ) ( y_v + dy_v over dv dv - y_w ) ~=~ ( x_v + dx_v over dv dv- x_w ) ( y_u + dy_u over du du- y_w )

( y_v - y_w) dx_u over du du ~+~ ( x_u - x_w ) dy_v over dv dv ~=~ ( y_u - y_w) dx_v over dv dv ~+~ ( x_v - x_w ) dy_u over du du

Now, from w = w( u,v ) , we get

dw = {partial w} over {partial u} du + {partial w} over {partial v} dv

In this case, dw = 0, so

-{{~{partial w} over {partial u}~} over {{ {partial w} over {partial v}}}} du ~=~ dv

Substitute into the above, then tidy up:

{ {partial w} over {partial v}}( ( x_w - x_v ) dy_u over du ~-~ ( y_w - y_v) dx_u over du) ~=~ {{partial w} over {partial u}}( ( x_u - x_w ) dy_v over dv ~-~ ( y_u - y_w) dx_v over dv)	(7)

NOTES:
1. this is not independent of 5 & 6. This can be seen by dividing those 2 equations, then cancelling the common term and cross multiplying the denominators.
2. These equations are telling us that the slopes of the axes (ie {dx} over {du} , etc) must head off in a direction that keeps the points in a nomogram lined up.

So, the coordinates of any index line must satisfy equations 3, 5 & 6. This information can be used to:
1. help determine an initial estimate
2. constrain the numerical solution for a smoother nomogram

TODO: this is just the first term of a Taylor's series about the index line. Is it helpful to go further?

As an aside, consider equation (7) above for the special case of a nomogram with 3 parallel lines, i.e. where x is fixed for each axis, so {dx_u over du} ~= ~ 0 " and " {dx_v over dv} ~= ~ 0 .
This leaves:

{ {partial w} over {partial v}} ( x_w - x_v ) dy_u over du ~=~ {{partial w} over {partial u}} ( x_u - x_w ) dy_v over dv

Now take the natural log of both sides:

ln{ {partial w} over {partial v}} ~+~ ln(( x_w - x_v ) dy_u over du) ~=~ ln{{partial w} over {partial u}} ~+~ ln(( x_u - x_w ) dy_v over dv)

Differentiating with respect to u then v leaves only the leftmost term on each side:

{partial^2 ln{ {partial w} over {partial v}}} over { partial u ~partial v } ~=~ {partial^2 ln{{partial w} over {partial u}}} over { partial u ~partial v }	(8)

Thus, with equation (8) above we have a derived Paul de Saint-Robert’s criterion for the feasibility of a 3 parallel line nomogram – see reference [3].
# Which way are the axes oriented?
If we assume that the u scale increases (varies from umin to umax) as the y coordinate increases, and if we define
w_0 = w(u_min, v_min)
w_1 = w(u_max, v_min)
w_2 = w(u_min,v_max)
then the w scale increases upwards if w_1 > w_0 and the v scale increases upwards if (w_1 > w_0) = (w_2 > w_0) , i.e. w1 and w2 are both less than, or both greater than w0, as can be seen in the diagrams below:

vmax
umax
umin
w0
w1
w2
Here, the v scale increases upwards and both w1 and w2 must be greater than w0 if the w scale increases upward, or they both must be less than w0 if the w scale increases downwards.
Here, the v scale increases downwards and w0, must lie between w1 and w2. As above, w1 is greater than w0 if the w scale is increasing upwards, otherwise w1 is less than w0 if the w scale increases downwards

umax

vmin
umin
w0
w1
w2
vmax

vmin

# Initial Estimate
The optimisation algorithms need a good initial guess to converge on the optimal solution nomogram.
## A Simple Linear Estimate
Try to approximate the true nomogram with a simple linear one as follows:

x
y

v scale
A
B
C
D
E
F
G
H
v scale
w scale
u scale

The u, v & w scale lines are respectively AD, CF & BE.
Point A is at (0,0), C is at (1,0), D is at (0,1), and F is at (1,1), u varies from umin to umax & v from vmin to vmax. Four index lines are shown, and their points of intersection with the scale lines are marked A to H. The x coordinate of u is given by the function xu = xu(u), with similar functions for the y coordinate and the variables v & w.
We have for the equations of each of the scale lines:
u_x = 0
u_y = {u -u_min} over {u_max - u_min}
v_x = 1
w_x = c + %alpha_wx( w-w_B )
w_y = %alpha_wy ( w-w_B ) ,
where c, αwx and αwy are constants that are not yet determined.

If the v scale has vmax at the top, then define
v_top = v_max, ~~~ v_bottom = v_min
Otherwise, the v scale is reversed so that vmin is at the top, then define:
v_top = v_min, ~~~ v_bottom = v_max
We can now write
v_y = {v - v_bottom} over { v_top - v_bottom }
G is where the scale line for w intersects the index line for u=umax, v=vbottom, so wG=w(umax, vbottom), and similarly, wH=w(umin,vtop), wB=w(umin,vbottom) & wE=w(umax,vtop).
Note that point B is at (c,0), E is at ( c + %alpha_wx( w_E - w_B )", " 1 ), and G & H intersect the diagonal index lines, so
%alpha_wy = 1 over { w_E-w_B }	(9)

c+ %alpha_wx( w_H - w_B ) " = " %alpha_wy( w_H - w_B ) " = " {w_H - w_B} over { w_E - w_B }	(10)

c+ %alpha_wx( w_G - w_B ) " = " 1 - %alpha_wy( w_G - w_B ) " = 1 - " {w_G - w_B} over { w_E - w_B } " = " { w_E -w_G } over { w_E - w_B }	(11)

Equation (9) gives %alpha_wy and (10) & (11) can be solved to give:
%alpha_wx = {w_E - w_G - w_H + w_B} over { (w_E-w_B)(w_G - w_H) }
c " = " {w_H - w_B} over { w_E - w_B }" - " %alpha_wx( w_H - w_B )

A more sophisticated approach might be to find quadratic and cubic approximations for the scale lines, and using the derivative equations to find the required coefficients.
Problems that might occur:
1. this approximation can leave wB & wE outside the unit square.
   A simple way to address this is to clip the values so that 0 ≤ wB, wE ≤ 1
2. wG might equal wH, leading to a division by zero in the equation above.
   A simple way to address this is to make the w scale line vertical, or use the derivative equations that are described below.

## The approximation error
Given a candidate set of the u,v & w scales, determine an error function as E = sum from{i,j=0} to{N} e_ij ^2 , where eij is the error of the line determined by the points ui & vj, where ui & vj refer to the ith and jth Chebyshev nodes on the u & v scale lines.
If the u,v & w scales are approximate, the point corresponding to w_ij = w( u_i, v_j) will not lie on the index line connecting ui & vj. The distance of wij from the line is given by equation (2) on page 4, and the coordinates are found from the equations ux(u), etc.
We can extend this idea by demanding also that the slopes of the scale lines must have minimum error as well.
Consider figure 1 below where a line AB intersects the u & v scale lines at points (xu, yu) & (xv, yv)

Figure 1: intersection line

u
w
v
A
B
w1=w(u+∆u, v+∆v)

Δu
Δv
A’
B’

Rewriting (2) above we have the error, e0. For the line AB:
e_0 " = " { x_u y_v + x_w y_u + x_v y_w - x_w y_v - x_u y_w - x_v y_u } over sqrt{ {(x_u - x_v)} ^{2} + { (y_u - y_v) } ^ 2}
For any nearby line, the intersection coordinates at A’B’ are given by
( x_u( u ) + dx over du %DELTA u , y_u( u ) + dy over du %DELTA u ) and ( x_v( v ) + dx over dv %DELTA v , y_v( v ) + dy over dv %DELTA v )
where Δu and Δv are the small deviations along the u & v scale lines. The point w1 is the point on the w scale line corresponding to w for the values of u+∆u & v+∆v, and has coordinates ( xw(w(u+∆u , v+∆v)), yw(w(u+∆u , v+∆v)) ). If the scale lines are so far only approximate, w1 will normally not lie on the line A’B’.
The error for the line A’B’ is the distance of the point w1 from A’B’ and nearby lines, given by
E ~=~ e_0 ~+~ {partial e} over {partial u} %DELTA u ~+~ {partial e} over {partial v} %DELTA v

Differentiating the expression for e,
{partial e} over {partial u} " = " {partial over {partial u}}({ x_u y_v + x_w (y_u - y_v) + (x_v - x_u) y_w - x_v y_u } over sqrt{ (x_u - x_v) ^2 + (y_u - y_v) ^ 2 })

{partial e} over {partial u} " = " { dx_u over du (y_v - y_w) ~+~ {partial w} over {partial u} (dx_w over dw (y_u - y_v) ~-~ (x_u - x_v) dy_w over dw ) ~-~ (x_v - x_w) dy_u over du } over sqrt{ (x_u - x_v) ^2 + (y_u - y_v) ^ 2 } newline ~-~ { e_0 {( (x_u - x_v){dx_u over du} ~+~ (y_u - y_v){dy_u over du} )} } over { (x_u - x_v) ^2 + (y_u - y_v) ^ 2 }
where e0 is the error defined above.
Similarly, for v:
{partial e} over {partial v} " = " {partial over {partial v}}({ x_u y_v + x_w (y_u - y_v) + (x_v - x_u) y_w - x_v y_u } over sqrt{ (x_u - x_v) ^2 + (y_u - y_v) ^ 2 })

{partial e} over {partial v} " = " { dx_v over dv (y_w - y_u) ~+~ {partial w} over {partial v} (dx_w over dw (y_u - y_v) ~-~ (x_u - x_v) dy_w over dw ) ~-~ (x_w - x_u) dy_v over dv } over sqrt{ (x_u - x_v) ^2 + (y_u - y_v) ^ 2 } newline newline ~+~ { e_0 {( (x_u - x_v){dx_v over dv} ~+~ (y_u - y_v){dy_v over dv} )} } over {(x_u - x_v) ^2 + (y_u - y_v) ^ 2 }

When the errors e_0 ", " {partial e} over {partial u} " and " {partial e} over {partial v} are reduced to zero, these equations match the equations found in the section Derivatives of the scale lines on page 5.

This gives an error function for the (u,v) pair:

E_ij ~=~ e_0^2 ~+~ %mu_u({partial e} over {partial u})^2 ~+~ %mu_v({partial e} over {partial v})^2	(12)

, where %mu_u and %mu_v are some scaling constants.

- Create an error function by summing the squares of all errors over all Chebyshev nodes for u & v
- Use SciPy to minimise this error as a function of the node coordinates
- if the minimum error is acceptably small, then the solution is the nodes that define the nomogram, otherwise a solution cannot be found.

### There are some issues that need to be resolved in the above scheme:
1. The number of error calculations is of the order O(n2), where n is the degree of the polynomial, but the number of coordinates to fix is of the order O(n). If n is large, pruning the number of error calculations can improve computation speed. (This doesn’t work.)
2. If the distance between the tic marks of one of the scale lines is non-linear, then the Chebyshev nodes are bunched together at some part in the line, and spread out at another. This could reduce the accuracy of the error calculations. Using log scales helps if the scales are logarithmic.
Instead of defining the Chebyshev nodes on the values of u (or v or w), define them on some function lu(u) of the scale line, and similarly for lv(v) & lw(w)
… TBC …

## The measurement error
These 2 nomograms for the equation 1/w ~=~ 1/u ~+~ 1/v have different shapes. Is one better than the other?

Our intuition tells us a good nomogram must fill its area as much as possible to make readings accurate.

If we have a formula
w = w(u,v), ~~ where ~~ u_min <= u <= u_max,~~ v_min <= v <= v_max
we can determine the position of the u, v & w curves at the Chebyshev nodes, and from there generate the curves of the nomogram.
To get best accuracy, we want the nomogram to be as large as possible, but lie inside the area available.
Available methods are:
1. Tie the ends of the outer scale line to the unit square.
   This is the simplest method, but doesn’t take advantage of V-type nomograms.
2. Minimise alignment error. If the scale lines are as tall as possible, the corresponding scale variable takes the maximum length. So an alignment error of, say, 0.1mm will correspond to the smallest possible error in the scale variable. Also, if the scale lines are separated as widely as possible, any parallax type errors will be minimised.

Even with a perfectly constructed nomogram, a perfectly drawn index line is not possible in practice. If we assume some tolerance in the position of the index line, we want the measurement errors of each of the scale variables to be as small as possible.

In figure 2 below, index line AA intersects the u scale line:

A’
u
ΔS

θ

A
Δa
A
A’

Figure 2: index lines intersecting the u scale line

The measured line A’A’ has an offset error Δa from the true line AA and it intersects the u scale a distance of ΔS from the exact position.
For a given Δa, we want the corresponding Δu to be as small as possible. Mathematically, we want to minimise du over da subject to the nomogram fitting inside the unit square.

We can write these 2 equations for ΔS:
%DELTA S ~=~ {%DELTA a} over {sin(%theta)}
%DELTA S = sqrt{{{d x_u} over { d u }}^2 ~+~ {{d y_u} over { d u }}^2 } %DELTA u

For any given (u,v) pair, the line AA intersects the points (xu(u), yu(u)) and (xv(v), yv(v)), and at the intersection, the u scale line is aligned with the vector ( {d x_u} over { d u },~{d y_u} over { d u } ).
Now use the definition of the vector cross product to write:
sin( %theta ) = { {dx_u} over {du} (y_u(u) - y_v(v)) ~-~ {dy_u} over {du}(x_u(u) - x_v(v)) } over { sqrt{({d x_u} over { d u })^2 ~+~ ({d y_u} over { d u })^2 } sqrt{ (x_v(v) - x_u(u))^2 ~+~ (y_v(v) - y_u(u))^2 } }

Combine the above to eliminate ΔS and sin(θ):
%DELTA a ~=~ { {dx_u} over {du} (y_u(u) - y_v(v)) ~-~ {dy_u} over {du}(x_u(u) - x_v(v)) } over { sqrt{({d x_u} over { d u })^2 ~+~ ({d y_u} over { d u })^2 } sqrt{ (x_v(v) - x_u(u))^2 ~+~ (y_v(v) - y_u(u))^2 } } ~ sqrt{{{d x_u} over { d u }}^2 ~+~ {{d y_u} over { d u }}^2 } %DELTA u
%DELTA a ~=~ { {dx_u} over {du} (y_u(u) - y_v(v)) ~-~ {dy_u} over {du}(x_u(u) - x_v(v)) } over { sqrt{ (x_v(v) - x_u(u))^2 ~+~ (y_v(v) - y_u(u))^2 } } %DELTA u

Rearrange this and take the limit:

{d u} over {d a} ~=~ { sqrt{ (x_v(v) - x_u(u))^2 ~+~ (y_v(v) - y_u(u))^2 } } over { {dx_u} over {du} (y_u(u) - y_v(v)) ~-~ {dy_u} over {du}(x_u(u) - x_v(v)) }	(13)

Note that the reciprocal of this is the cross product of two vectors, x´ and n, where x´ is ({d x_u} over { d u },~{d y_u} over { d u }) which is the rate of change of distance in the direction of the u scale line. (It’s a velocity vector.) The vector n is {( y_u(u) - y_v(v) ,~ x_u(u) - x_v(v) )} over { sqrt{ (x_v(v) - x_u(u))^2 ~+~ (y_v(v) - y_u(u))^2 } } which is a unit vector along the index line AA.

n
x´

Figure 3: The cross product of u' and n
The magnitude of this vector is the area created by the cross product between x´ and n as shown in figure 3 above.

So minimising equation (13) is equivalent to maximising this area (because it’s a reciprocal).
This means we want to:
1. make x´ as long as possible, i.e. stretch the scale lines as much as possible. Remember, n is a unit vector, so its length is fixed.
2. make the vectors as close to perpendicular as possible, i.e. make the scale lines as far apart as possible.

This matches our intuition on what makes a better nomogram.

Now consider an index line AA crossing 3 scale lines u, v & w:

A
A
A’
A’

u
v
w

Δa
Δw
Δu
Δv

A’A’ is the measured line, and has an offset error Δa from the ideal line AA.
Δu, Δv & Δw are the measurement errors in the scale variables.

Recalling (13) above,

{%DELTA u} ~=~ { sqrt{ (x_v(v) - x_u(u))^2 ~+~ (y_v(v) - y_u(u))^2 } } over { {dx_u} over {du} (y_u(u) - y_v(v)) ~-~ {dy_u} over {du}(x_u(u) - x_v(v)) } %DELTA a ~=~ %xi_u %DELTA a

with a similar expressions for ξv.

We can write:

%DELTA w ~=~ {{{partial w} over {partial u}} %DELTA u} ~+~ {{{partial w} over {partial v}} %DELTA v}

Now substitute Δu & Δv:
%DELTA w ~=~ %DELTA a ( {partial w} over {partial u} %xi_u ~+~ {partial w} over {partial v} %xi_v )

Taking the limit as Δa approaches zero:

dw over da ~=~ {partial w} over {partial u} %xi_u ~+~ {partial w} over {partial v} %xi_v	(14)

We now we have expressions that can be optimised to generate the best nomogram for the given function.
This is not sufficient, however, because this would create a nomogram of infinite size.
We need a cost function to penalise nomograms that are larger than the specified paper area.

Consider this cost function:

c(t) " = " exp(40*(-0.3-t)) ~+~ exp(40*(t-1.3))	(15)

Its value is very close to 1 in the central region of the unit square, but near the edges it quickly grows positive as it approaches the boundaries at 0 or 1 as shown in 4 below.

Figure 4: Cost vs position inside unit square
Define the cost of the nomogram due to its shape as
{dw} over {da} ( c(x_u) + c(y_u) + c(x_v) + c(y_v) + 1) ,

where { dw } over { da } is defined in equation (14} above. The c(x) and c(y) terms are from (15) above and are the costs of the x & y coordinates of the Chebyshev nodes on the u & v scale lines. We can add this term to the overall cost function for the nomogram given by (12) above

Now we can minimise the shape cost of a nomogram by increasing the area up to the edges. Near the edges, the costs start to increase rapidly beyond the boundary of the unit square. Thus we can achieve a balance where the nomogram has the smallest measurement error for the specified nomogram size.

## Further Investigations
#### Tabulated data
Since the construction method already outlined uses a least-squares approach, it should be possible to construct a nomogram from tabulated data.
Instead of using ui, vj & wij derived from equations, use these values stored in the tabulated data.

#### Scales Transformations
Eversham [3], p 203, “Džems-Levi shows that there are three, and only three, projectively distinct scales for x. They are:
alignl f_1( x) ~=~ e^{ax}~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~ newline alignl f_1( x) ~=~ ax~~~ newline alignl f_1( x) ~=~ tan(ax)

# References
1. PyNomo documentation
2. https://deadreckonings.files.wordpress.com/2009/07/creatingnomogramswithpynomo.pdf
3. The History and Development of Nomography, H. A. Eversham
4. “Barycentric Lagrange Interpolation”, Jean-Paul Berrut & Lloyd N. Trefethen, SIAM REVIEW Vol. 46, No. 3, pp. 501–51
5. Spectral Methods in Matlab, Lloyd N. Trefethen,
   http://www.comlab.ox.ac.uk/oucl/work/nick.trefethen
6. Introduction to approximating functions with Chebyshev polynomials https://www.youtube.com/watch?v=F_43oTnTXiw
   https://blogs.mathworks.com/cleve/2018/12/10/explore-runges-polynomial-interpolation-phenomenon/
   https://demonstrations.wolfram.com/RungesPhenomenon/